## Slide 1
A D U DEWMINI
D/ENG/23/0160/BM
EARLOBE-BASED WEARABLE
FOR EARLY DETECTION OF SEPSIS-RELATED VITAL
SIGNS
ABNORMALITIES IN
BEDRIDDEN PATIENTS

## Slide 2
  Problem Identification
  Aim
  Objectives
  Market survey
  Components
  system Design
  Circuit Diagram
  Solid work design
  PCB design
  Stimulation and results
  Problems encountered
  Cost estimation
CONTENT

## Slide 3
  Delayed Detection of Sepsis in Bed Patients
  Lack of Continuous Monitoring
  Uncomfortable and Inconvenient Monitoring Methods
  Need for a Non-Intrusive and Comfortable Solution
  Risk of Caregiver Dependence
  Affordable and Accessible Health Monitoring
PROBLEM IDENTIFICATION

## Slide 4
To design and develop a compact, non-invasive earlobe-mounted medical device that continuously monitors heart rate, blood oxygen saturation (SpO₂), and body temperature using integrated sensors, to detect early physiological signs associated with sepsis. The system incorporates a color-coded display and alarm mechanism to provide timely alerts for abnormal vital signs, enhancing early intervention and patient safety in home-care settings for bedridden individuals..
AIM

## Slide 5
Device Design and Sensor Integration
Real-Time Alert and Monitoring System
To design and develop a compact, non-invasive earlobe-mounted device that continuously monitors heart rate, SpO₂, and body temperature using integrated sensors..
To implement a real-time alert system with color-coded visual indicators and audible alarms to notify caregivers of abnormal vital signs associated with early signs of sepsis.
OBJECTIVES
Wireless Communication and Data Transmission
To ensure the device is lightweight, comfortable for continuous wear, and operates efficiently with long battery life for reliable monitoring.

## Slide 6
Patients at increased risk of developing sepsis, those in home-care settings
Bedridden patients requiring continuous vital monitoring
Home-care patients with limited access to clinical observation
Elderly individuals more vulnerable to sepsis-related complications
Post-operative patients during recovery at home
Chronically ill or immunocompromised individuals at risk of infection
Patients with limited mobility or neurological impairments, where early signs of sepsis may go unnoticed
Target Group

## Slide 7
AVAILABLE PRODUCTS
Existing Devices for Early Sepsis Detection:
  IntelliSep Sepsis Test (Cytovale) – 8 min detection using immune response analysis.
  Sepsis aiMarker™ (Biocogniv) – AI-based prediction up to 72 hours in advance.
  KATE AI Sepsis (Mednition) – 118% improved early detection in emergency triage.
  Patient Status Engine (Isansys Lifecare) – Wearable smart patch for continuous monitoring.
MARKET SURVEY

## Slide 8
AVAILABILITY OF PATENT RIGHTS
  Multiple patents exist for biomarker kits, AI-based models, and wearable biosensors.
  Patent Gaps- Opportunities for home-based monitoring, AI integration, and non-invasive diagnostics.
  Freedom to Operate (FTO) Analysis required to ensure no patent infringement.
MARKET SURVEY

## Slide 10
VALUE ADDITION FOR THE DEVICE
  Affordable Home Monitoring-Unlike hospital-based systems, your device allows continuous sepsis monitoring at home.
  Wearable & Adjustable Fit-Velcro strap for comfort ensures a secure and customizable fit for different patients.
  Real-Time Alerts- improves detection accuracy while reducing false alarms.
  User-Friendly Design- Plug-and-play operation, easy-to-read interface, and smartphone connectivity for caregivers.
  Non-Invasive Alternative-Unlike blood-based biomarker tests, your device detects sepsis risk using real-time physiological monitoring.
MARKET SURVEY

## Slide 11
  ESP32-Processes sensor data, manages alerts
  MAX30102 Pulse Oximeter Sensor- Heart rate₂ and oxygen saturation
  MLX90614 Infrared Temperature Sensor-measure-Non-contact body temperature
  LCD Display
  Mini Buzzer (SP001)
  LED - for visual display
  3.7V Li-ion Rechargeable Battery
  Resistors & Capacitors
COMPONENTS

## Slide 12
ear
MAX30102
Pulse oximeter sensor
MLX90614
Tempreature sensor
ESP32
Data transmission
LCD Display
LED Indicater
Buzzer
Earlobe Sensor Unit
Data Display and Alert
SYSTEM DESIGN
Green LED: Indicates normal/healthy readings.
        SpO₂: 94%-100%
        Heart rate: 60-90 bpm
        Body temperature: 36°C-37.5°C
      Yellow LED: Signals a warning that one or more vitals are approaching abnormal ranges.
        SpO₂: 90%-94%
        Body temperature: 37.6°C-38°C
      Red LED: Signals a critical condition where intervention is needed immediately. For example:
        SpO₂: <90%
        Heart rate > 90 bpm
        Body temperature: >38°C or <36°C
        There is a audible alert from buzzer when red LED is on

## Slide 13
CIRCUIT DIAGRAM
EAR LOBE DEVICE

## Slide 14
CIRCUIT DIAGRAM

## Slide 15
SOLID WORK DESIGN
EAR LOBE DEVICE DESIGN
opening for temperature sensor
opening for MAX30102

## Slide 16
SOLID WORK DESIGN
DISPLAY SYSTEM
OPENINGS FOR LEDS
OPENING FOR LCD DISPLAY

## Slide 17
PCB DESIGN
ESP32
MLX90614
MAX30102

## Slide 18
3D View

## Slide 19
STIMULATION AND RESULTS
ESP32
MLX90614
MAX30102
Red LED was on and buzzer audible alert when temperature was below 36 celsius

## Slide 20
STIMULATION AND RESULTS
ESP32
MLX90614
MAX30102
Green LED was on when temperature was > 36 celsius and<37.5 celsius

## Slide 21
STIMULATION AND RESULTS
ESP32
MLX90614
MAX30102
YellowLED was onwhen temperature was > 37.5 and <38 celsius

## Slide 22
  Library Issues-Despite downloading the required MAX30102 libraries, Arduino IDE showed "No such library" errors.
  Code Execution Challenges- After obtaining the code from GitHub, the code executed, but the sensor was not captured.
  Sensor Initialization Loop-The sensor repeatedly showed "Initializing" but failed to work.
  Circuit Modification Attempts- Made changes to the sensor circuit, but the issue persisted.
PROBLEMS ENCOUNTERED

## Slide 25
ESP32 | 1100
MAX30102 Pulse oximeter sensor | 790
LCD Display | 470
Buzzer | 50
3 LED’S | 60
3.7V Li-ion Rechargeable Battery | 1000
resistors | 80
TOTAL COST | 3510
COST ESTIMATION

## Slide 26
THANK YOU